## Slide 1: Cognitive Relay: Detecting Spectrum Holes in a Dynamic Scenario
System Model
Cross layer optimization
Receiver model
Energy detection
Learning
Modelling channel access
as discrete time
discrete state Markov process
PU subchannels N
Multiband sensing through
scanning
State transition probabilities (a , b )
Utilization probability u
Ankit Kaushik, Marcus Müller and Friedrich K. Jondral
{ankit.kaushik, friedrich.jondral}@kit.edu, {marcus.mueller@student.kit.edu}
Karlsruhe Institute of Technology
Communications Engineering Lab
Scenario
Cognitive Relay (CR) is a network element of the SU system
Supports wireless services for devices operating indoor
Enables dynamic access to increase spectral efficiency
Implementation and User Interactions
Demonstrator Setup
Analysis
Introduction and Motivation
Dynamic Spectrum Access (DSA) is one of the many applications of cognitive radio.
Main tasks for a DSA operating as Secondary User (SU):
Sensing (Learning) and intelligent access (Act)
Avoid interference to the Primary User (PU)
Purpose of this work:
Realize the cognitive concepts over the hardware
Use sophisticated algorithms to reduce the time constraints and computational complexity
Demonstrate the radio in a real scenario
Conclusion and Future Work
Cognitive radio implementation in a dynamic scenario
Potential to sense non-contiguous multiple band simultaneously over low cost hardware
Capable to learn and interact with its environment
Considering other scenarios such as Overlay Systems
– Spatial separation of the PU and SU systems (transmission power control)
Cooperation with other the CRs
T (Y) test statistics
K number of samples
Y [n] received waveform
X [n] transmitted waveform
W [n] noise waveform
 threshold, determined using constant false alarm
Test scenario | GSM channels at 1800 MHz
Shared Access | Interweave
Hardware | USRP N210
Multiband sensing Software defined architecture | GNU Radio
Detection of spectral holes | Time slots
Estimation of model parameters (a, b ) | Maximum likelihood estimation
Channel ranking | u = [u1, u2, ..., uN ]
^
^
MAC Layer
PHY Layer
u
time/s
Channels /MHz
Channels /MHz